## Slide 1: Initial Planform Assumptions
Main wing is inline with the bottom of T-Tail
Sweep angle does not appear to be specified. Will assume that this is roughly 10 degs
Front of the wing is located at coordinates [0, 0, 0]
Elastic Axis will be placed at 25% chord for all aero surfaces

## Slide 2: Dimensions needed for Creation
Span | 13.53m (semi 6.765m) – 44.4ft
Area | 11.89m2 – 128ft2
Chord | .8787
Sweep | 10 deg
Wing
V-Tail
Span | 1.609m - 5.28 ft
Area | 1.691m2 - 18.2ft2
Chord | 1.051m
H-Tail
Span | 3.048m (semi 1.524m) - 10 ft
Area | 3.01m2 (semi 1.505m2)– 32.4ft2
Taper | 10 deg
Root Chord | .8787
Location of H-Tail is 26’ from the front of the aircraft
Assumed that cg is located at TE of root
CG is 9.7’ from nose. Chord is .8787m so distance from LE of root to TE of Tail is 5.847m
By knowing the chord dis of H-Tail, the EA is known

## Slide 3: Coordinates Assuming 10 deg Sweep

## Slide 4: Mass Distributions
Structural Weight | 920.79 kg
Main Wing | 205.47 kg
H-Tail Weight | 63.96 kg
Rotor Group + Propulsion | 1116.74 kg
Fuel System | 281.23 kg
Drive System Weight | 71.67 kg
Systems Weight | 301.64 kg
Total Weight | 2961.5 kg
Adding up all mass contributions except empty weight = 6529 lbs. Will consider that the total for now
Rotor group and propulsion weight is combined. Will be divided into 8 for each rotor: 139.5925 per rotor

## Slide 5: Structural Mass Breakdown
Structural Weight | 920.79 kg
Main Wing | 205.47 kg
H-Tail Weight | 63.96 kg
Rotor Group + Propulsion | 1116.74 kg
Fuel System | 281.23 kg
Drive System Weight | 71.67 kg
Systems Weight | 301.64 kg
Total Weight | 2961.5 kg
T-Tail: (63.96+ .10*920.79)/ (1.609 + 2*(1.524/cos(10))) = 33.17
Main Wing: (205.47 + .40*920.79)/ (2*(6.765/cos(10))) = 35.062
Fuselage Contribution: (.5*920.79)/(7.486) = 61.5
Misc. Lumped Mass to get desired CG: 654.54 kg

## Slide 6: Rotor Lumped Masses
Rotor group and propulsion weight is combined. Will be divided into 8 for each rotor: 139.5925 kg/rotor
Assumed location of lumped mass is .4m forward and .3 m downward from EA locationv
2.225m distance between rotors on wings
[1.53, 6.765, -.3]
[.895, 4.54, -.3]
[0.26, 2.315, -.3]
[5.057, 1.525, 1.309]

## Slide 7
Z cg should be -.64652m
X cg should also be .659m